## Slide 1: Predicting “Do Not Drive” Orders from Vehicle Recall Data
BUSINESS INTELLIGENCE · TEAM 6 · PROJECT UPDATE
Team 6 · Course 39122
Notes: About 10 seconds. Introduce the team and the question: can we predict which vehicle recalls will escalate to a Do Not Drive advisory? Then move straight to the context.

## Slide 2: Most recalls are routine. A few mean “stop driving this vehicle now.”
1 · CONTEXT AND QUESTIONS
A Do Not Drive (DND) advisory is the most urgent recall signal. It is rare, and it is easy to miss in a quarter-million recall records.
Q1 · Feasibility
Can we predict a DND advisory from recall data?
Q2 · Risk drivers
Which manufacturers, components and wording signal risk?
Q3 · Triage use
Is it precise enough to help reviewers prioritize?
Notes: About 30 seconds. Most recalls are routine, but a Do Not Drive advisory means a vehicle should not be driven at all. It is rare and hard to spot. We ask three things: can we predict it, what drives it, and could it support triage.

## Slide 3: NHTSA recall files, cleaned to 252,573 records
2 · DATA AND VARIABLES
252,573
rows after sanitizing 327,036 raw rows (pre- and post-2010 files)
18,999
recall campaigns, each with many rows
0.83%
of rows carry a DND advisory (the target)
Inputs: recall description text (1,000 TF-IDF terms), component, manufacturer, “influenced by,” and log of potentially affected units.
Split by campaign (70/15/15) so rows from one campaign never land in both training and test.
Notes: About 45 seconds. Two NHTSA flat files, cleaned from 327,036 to 252,573 rows across 18,999 campaigns. Only 0.83 percent are Do Not Drive. Inputs are the recall text, component, manufacturer, who influenced the recall, and the number of vehicles affected. We split by campaign to prevent leakage.

## Slide 4: Campaign-grouped split: 70% train, 15% validation, 15% test
2 · DATA AND VARIABLES
Split
Rows
DND rows (rate)
Train
189,615
1,248 (0.66%)
Validation
29,055
266 (0.92%)
Test
33,903
593 (1.75%)
Splitting by campaign keeps related rows together, but it also means the DND rate differs by split. We keep that in mind when reading results.
Notes: About 20 seconds. This is the partition. Same campaign never crosses splits. A side effect is that the test set has a higher Do Not Drive rate than training, which matters when we interpret model scores later.

## Slide 5: DND is rare, and its rate shifts across the splits
3 · DESCRIPTIVE VISUALIZATIONS
Share of rows with a DND advisory
Train
0.66%
Validation
0.92%
Test
1.75%
About 1 in 120 rows overall (0.83%). Accuracy alone would be meaningless here, so we judge models with precision-recall measures.
Notes: About 35 seconds. First pattern: class imbalance. Only 0.83 percent of rows are Do Not Drive, and the rate climbs from 0.66 percent in training to 1.75 percent in test. A model that says never DND is 99 percent accurate, so we use precision, recall and PR-AUC.

## Slide 6: Manufacturer and vehicle cues carry the strongest DND lift
3 · DESCRIPTIVE VISUALIZATIONS
DND rate vs. the 0.66% training baseline (training data)
Yamaha (maker)
84.8x
Mazda (maker)
48.9x
“dodge” in text
15.3x
“bmw” in text
12.9x
“performance” in text
12.4x
“steering” in text
2.4x
Lower-risk cues: “possibly” 0.25x, “2020” 0.33x, “battery” 0.51x. Large lifts rest on small groups, so we treat them as signals, not proof.
Notes: About 45 seconds. Second pattern: which features separate DND from routine recalls. Yamaha and Mazda recalls are dramatically more likely to be DND, then vehicle names like Dodge and BMW. Steering wording is a smaller but broad signal. Protective cues like the word possibly point the other way. Caveat: some groups are small.

## Slide 7: Model-centered: LightGBM on text and recall attributes
4 · PROJECT DIRECTION AND PROPOSED METHOD
0.73
test PR-AUC (ROC-AUC 0.93)
92%
precision at the 0.5 threshold
47%
recall: 276 of 593 test DND rows caught
Honest caveat: validation PR-AUC was only 0.15, so results are not yet stable across splits.
Next: tune thresholds for recall, calibrate scores, explain predictions with SHAP, then an optional reviewer triage queue.
Notes: About 55 seconds. Our direction is model-centered. A LightGBM classifier on TF-IDF text plus component, manufacturer and affected units. The first baseline reaches 0.73 PR-AUC and 92 percent precision on test, but only 47 percent recall, and validation PR-AUC was just 0.15, so we are not claiming stability yet. Next: threshold tuning, calibration, SHAP explanations, and possibly a triage queue for reviewers. Then take questions.